## Slide 1: Lecture-06

## Slide 2: Addressing Modes
Immediate
Direct
Indirect
Register
Register Indirect
Displacement (Indexed)
Stack

## Slide 3: Immediate Addressing
Operand is part of instruction
Operand = address field
e.g. ADD 5
  Add 5 to contents of accumulator
  5 is operand
No memory reference to fetch data
Fast
Limited range

## Slide 4: Immediate Addressing Diagram
Operand
Opcode
Instruction

## Slide 5: Immediate Addressing
Example : LOAD #5 // AC 5
Add #7 // AC  AC+7

## Slide 6: Direct Addressing
Address field contains address of operand
Effective address (EA) = address field (A)
e.g. ADD A
  Add contents of cell A to accumulator
  Look in memory at address A for operand
Single memory reference to access data
No additional calculations to work out effective address
Limited address space

## Slide 7: Direct Addressing Diagram
Address A
Opcode
Instruction
Operand
Memory

## Slide 8: Direct Addressing

## Slide 9: Indirect Addressing (1)
Memory cell pointed to by address field contains the address of (pointer to) the operand
EA = (A)
  Look in A, find address (A) and look there for operand
e.g. ADD (A)
  Add contents of cell pointed to by contents of A to accumulator

## Slide 10: Indirect Addressing (2)
Large address space
2n where n = word length
May be nested, multilevel, cascaded
– e.g. EA = (A) or EA=@A Look in A, Find address(A) and look there for operand
Multiple memory accesses to find operand
Hence slower

## Slide 11: Indirect Addressing Diagram
Address A
Opcode
Instruction
Pointer to operand
Operand
Memory

## Slide 12: Indirect Addressing

## Slide 13: Register Addressing (1)
Operand is held in register named in address filed
EA = R
Limited number of registers
Very small address field needed
  Shorter instructions
  Faster instruction fetch

## Slide 14: Register Addressing (2)
No memory access
Very fast execution
Very limited address space
Multiple registers helps performance
  Requires good assembly programming or compiler writing
  N.B. C programming
    register int a;
c.f. Direct addressing

## Slide 15: Register Addressing Diagram
Register Address R
Opcode
Instruction
Operand
Registers

## Slide 16: Register Addressing

## Slide 17
Register Indirect Addressing
C.f. indirect addressing
EA = (R)
Operand is in memory cell pointed to by contents of register R
Large address space (2n)
One fewer memory access than indirect addressing

## Slide 18: Register Indirect Addressing Diagram
 | Opcode | Register Address R | 
Instruction
Operand
Memory
Pointer to Operand
Registers

## Slide 19: Register Indirect Addressing

## Slide 20: Displacement Addressing
EA = A + (R)
Address field hold two values
  A = base value
  R = register that holds displacement
  or vice versa

## Slide 21: Displacement Addressing Diagram
Instruction
Operand
Memory
Pointer to Operand
 | Opcode | Register R |  | Address A
Registers
+

## Slide 22: Displacement Addressing

## Slide 23: Relative Addressing
A version of displacement addressing
R = Program counter, PC
EA = A + (PC)
i.e. get operand from A cells from current location pointed to by PC
For Example:
Load $A or Load A(PC) // AC M[PC+A]
Address location is relative to “PC”, this is called Relative Mode.

## Slide 25: Base-Register Addressing
A holds displacement
R holds pointer to base address
R may be explicit or implicit
e.g. segment registers in 80x86
Register= Base Register
Effective Address = content of BR + address part of instruction
EA = (Ri) + A
e.g. Load A(R1) // R1  M[R1 + A]

## Slide 27: Indexed Addressing
A = base
R = displacement
EA = A + R
Good for accessing arrays
– EA = A + R
– R++
Example: ADD R1, 20(R2) //R1 R1 + M[20+R2]